## Slide 1: Input Voltage Level
FSR 1

## Slide 2: Power converters shall convert 15 VDC to isolated 15 VDC.
Vin (V) | Vin,pp (mV) | Vout (V) | Vout,pp (mV)
9.1 | 200 | 15.1 | 400
15.1 | 500 | 15.0 | 400
20.9 | 500 | 14.9 | 400
27.0 | 500 | 15.3 | 500
33.040 | 578 | 14.887 | 264
35.804 | 503 | 14.887 | 264
Iout (mA) | Vout (V)
12 | 14.959
25 | 14.951
50 | 14.937
75 | 14.924
100 | 14.912
125 | 14.898
134 | 14.893
Vin = 9 V
Vin = 15 V
Vin = 21 V
Vin = 27 V

## Slide 3: Power converters shall convert 15 VDC to 3.3 VDC.
Vin (V) | Vout (V)
16.0 | 3.003
15.5 | 3.2997
15.0 | 3.2997
14.5 | 3.2995
Load (mA) | Vout (V)
0 | 3.2993
30 | 3.2952
50 | 3.2824
72 | 3.2812
95 | 3.2601
122 | 3.2512
153 | 3.2243

## Slide 4: Power converters shall convert 3.3 VDC to isolated 5 VDC.
Iout (mA) | Vout (V)
12 | 5.381
50 | 5.188
100 | 4.981
150 | 4.782
200 | 4.581
Vin (V) | Vin,pp (mV) | Vout (V) | Vout,pp (mV)
2.8 | 500 | 4.9 | 500
3.2 | 500 | 4.8 | 500
3.3 | 500 | 5.3 | 500
3.6 | 900 | 5.7 | 500
Vin = 2.8 V
Vin = 3.2 V
Vin = 3.3 V
Vin = 3.6 V

## Slide 5: System shall convert 15 VDC to isolated 15 VDC , 3.3 VDC, and isolated 5 VDC.
Converter​ | Vspec [V]​ | Vmin [V]​ | Vnom [V]​ | Vmax [V]​
2-Phase to 15V​ | 15.0​ | ​ | 15.0​ | ​
15V to Iso15V​​ | 15.0​ | 14.9​ | 15.1​ | 15.3​
15V to 3.3V​​ | 3.3​ | 3.2​ | 3.3​ | 3.3​
3.3V to Iso5V​​ | 5.0​ | 4.6​ | 5.1​ | 5.6​

## Slide 6: Power converters shall convert 120 VAC to 15 VDC.
Vin (VAC) | Vout (VDC)
118 | 15.0

## Slide 7: On/Off Functionality
FSR 2

## Slide 8: Relay shall toggle the motor with the relay signal.
Vin |  | 
5-40V | Contact Voltage | Rated up to required voltage
15V | Coil Voltage | 
5V | Relay Signal | 

## Slide 9: Digital to power shall convert the relay signal from 3.3 VDC to 5 VDC.
~0 V when button off 3.4 V before isolator 5.8V after isolator

## Slide 10: MCU shall toggle the relay signal to 3.3 VDC with the button signal.
Relay | 
On | Off
3.281V | -.045V

## Slide 11: Button shall toggle the button signal to 3.3 VDC with a button press.
Button | 
Not Pressed | Pressed
3.25V | -.048V

## Slide 12: System shall toggle the motor between on and off state with a button press.
On/Off Button

## Slide 13: Motor Runs at Correct Voltage
FSR 3

## Slide 14: Rectifier shall convert 120 VAC to 112 VDC.

## Slide 15: PWM Signals
FSR 4

## Slide 16: Power control shall invert three high and three low 5 VDC PWM signals into three modified sine waves.
Expected Line to Line Waveforms
Measured Line to Line Waveforms

## Slide 17: Digital to power shall convert three high and three low PWM signals from 3.3 VDC to 5 VDC.
U
V
W
3.4 V 6.0-6.2 V

## Slide 18: MCU shall generate three high and three low 3.3 VDC PWM signals with the knob signal.
U
V
W

## Slide 19: System shall change the motor speed with the knob signal.
Measured Line to Line Waveforms
Speed Knob

## Slide 20: Continued
Knob | 
Positions | Voltage
Low | -.045V
Middle | 1.603V
High | 3.285
PWM |  |  |  |  |  | 
Signal | Frequency (kHz) | Minimum Voltage | Maximum Voltage | Phase Offset (degrees) | Low Pot Value - Low Frequency | High Pot Value - High Frequency
1H | 1 | -0.13 | 3.65V | 0 | TRUE | TRUE
1L | 1 | -0.13 | 3.65V | 0 | TRUE | TRUE
2H | 1 | -0.13 | 3.65V | 120 | TRUE | TRUE
2L | 1 | -0.13 | 3.65V | 120 | TRUE | TRUE
3H | 1 | -0.13 | 3.65V | 240 | TRUE | TRUE
3L | 1 | -0.13 | 3.65V | 240 | TRUE | TRUE

## Slide 21: Motor On/Off LED
FSR 5

## Slide 22: MCU shall toggle the motor on/off LED signal to 3.3 VDC with the button signal.
~0 V when button off 3.4 V when button on

## Slide 23: System shall toggle the motor on/off LED between on and off states with the motor on/off signal.
Motor LED (blue) off when on/off button is off Motor LED (blue) on when on/off button is on
(motor is off) (motor is on)

## Slide 24: System On/Off LED
FSR 6

## Slide 25: MCU shall toggle the circuit on/off LED signal to 3.3 VDC when the board receives power.
3.4V when circuit is on

## Slide 26: System shall toggle the circuit on/off LED when the board is connected to power with the circuit on/off signal
System LED (red) off when 15 V not applied System LED (red) on when 15 V applied
(system is off) (system is on)

## Slide 27: Diagnostic Feedback
FSR 7

## Slide 28: Diagnostic feedback circuit shall transport the voltage, current, and temperature signals from across the isolation barrier to the MCU.
 | Input Voltage | Output Voltage
bus.v | 15 V | 3.9 V
ilim.v | 15 V | 3.9 V
ips.temp | 15 V | 3.9 V

## Slide 29: Power Control shall generate 60 VDC voltage, current, and temperature feedback signals.
 |  | Output Voltage | Notes
bus.v | voltage |  | 
ilim.v | current | 0 | Built for 30 A, 2 A results in zero
ips.temp | temperature |  |